## Slide 1
Finishing
Tom Wirsing
September 5, 2013

## Slide 2
Finishes are Comprised of Two Parts
Solids – The part which remains after the finish is “dry” and which provides protection
  Shellac
  Lacquer
  Urethane
  Oil
  Wax
Solvent or Diluent – The part which “liquefies” the finish, making it easier to apply
  Alcohol
  Lacquer thinner
  Mineral spirits
  Water
  Etc.
Exceptions: Not all oils and waxes require a solvent or diluent

## Slide 3
Two Classes of Finish
  Evaporative
  Reactive

## Slide 4
Evaporative: The molecular structure of the solids in the finish does not change as the finish “dries”. The finish can be re-dissolved by the solvent
Reactive: A chemical reaction takes place. The molecular structure of the solids changes as the finish “dries”. The finish cannot be re-dissolved by the diluent

## Slide 5
Examples:
Evaporative:
  Shellac
  Lacquer (non-catalyzed)
  Wax
Reactive:
  Varnish
  Some oils (those which permanently harden as they dry)
  All catalyzed finishes (catalyzed lacquers and varnishes, epoxy and acrylic resins)
Exceptions: Some oils are neither evaporative or reactive (mineral oil, olive oil, etc.)

## Slide 6
Advantages and Disadvantages of Evaporative and Reactive Finishes
Evaporative:
  Advantages: Easy to repair
  Disadvantage: Delicate, easily damaged, especially by solvent
Reactive:
  Advantages: Hard and tough, especially some of the newer catalyzed lacquers and varnishes
  Disadvantages: difficult to repair. In come cases impossible to repair, requiring complete removal and reapplication (sand down to bare wood and start again)

## Slide 7
Solvent vs. Diluent
A solvent dissolves the solids in the finish. The finish can be re-dissolved later (even years later)
A diluent “liquefies” the finish but does not (is unable to) dissolve the solids in the finish.

## Slide 8
Characteristics of Various Finishes
Wax
Oils
Oil with Additives such as Urethane
Shellac
Lacquer
Catalyzed Lacquer
Varnish
Catalyzed Varnish

## Slide 9
Wax
  Examples:
    Bees wax
    Carnauba wax
    “Hut”
    Prepared paste waxes (Briwax, Mylands, Liberon)
    Spray waxes (Pledge)
  Advantages:
    Exceedingly easy to apply
    Exceedingly easy to repair
    Non-toxic (after solvent has flashed off)
  Disadvantages:
    Minimal protection
    Some worse than nothing (Pledge)
  Note: Wax is usually an evaporative finish. Most wax finishes contain a solvent, such as mineral spirits, which softens the wax, making it easier to apply. The solvent usually evaporates after application, allowing the wax to harden.

## Slide 10
Oil
  Examples:
    Linseed oil
    Tung oil
    Vegetable oils
      Walnut oil
      Olive oil
    Mineral oil
  Advantages:
    Exceedingly easy to apply
    Exceedingly easy to repair
    Usually not toxic (see note below)
  Disadvantages:
    Very little protection, easily damaged
    Dull appearance
    Can become rancid (e. g. olive oil)
    Some never dry completely hard
    Darken the wood
  Note: Typically vegetable and mineral oils do not require a diluent. Some oils, such as linseed and tung, are somewhat reactive and may contain a diluent such as mineral spirits. They may also contain dryers, which can be toxic.

## Slide 11
Oils with Additives such as Urethane
  Examples:
    Watco Danish Oil
    Deft Deftoil
  Advantages:
    Easy to apply
    Relatively easy to repair
    Tougher than oils without additives
    Much better “build” than oils without additives
    Oils penetrate and give “depth” to the finish, while urethanes provide “build”, toughness and durability
    Usually food safe once completely dry
  Disadvantages
    Can be damaged by water, food, acid (e.g. citric acid)
    More difficult to repair than oils without additives
    Usually toxic until completely dry
    Unpleasant odor until completely dry
  Note: Oils with additives are reactive and are usually comprised of either linseed or tung oil with urethane additives. The diluent is usually mineral spirits (refer to manufacturers’ specifications)

## Slide 12
Shellac
  Examples:
    Super Blond
    Orange
    Garnet
    Dry (flake, button, seed)
    Canned (ready to use), e.g. Bull’s Eye/Zinsser
    French polish (shellac and oil, usually linseed)
    Etc.
  Advantages:
    Very clear
    Relatively easy to apply and repair
    Excellent sealer, compatible with oils, lacquer, varnish
    Non-toxic
    Soluble by alcohol, even when completely dry
    “Authentic” for antiques
  Disadvantages:
    Easily damaged by water, and especially by alcohol
    “Membrane” finish
    Limited shelf life after being dissolved in alcohol
  Solvent: Ethanol (ethyl alcohol)
  Note: Shellac is an evaporative finish.

## Slide 13
Lacquer
  Examples:
    Nitrocellulose (cellulose nitrate)
    Acrylic
    CAB (cellulose acetate butyrate) “water white”
    Non-catalyzed (traditional), pre-catalyzed, catalyzed
    Water based
  Advantages:
    Easy to apply, especially if sprayed (but requires considerable skill)
    Very clear
    Capable of attaining very high reflectivity, very glassy (piano finish)
    Soluble by lacquer thinner. Very easy to recoat, and relatively easy to repair (except catalyzed)
    Catalyzed lacquers are extremely tough, durable, clear
    Generally not toxic once completely dry
  Disadvantages:
    Tricky to apply, requires practice, skill
    Somewhat delicate: scratches easily (except catalyzed)
    “Membrane” finish
    Solvents and diluents are often quite toxic
    Catalyzed lacquers, while extremely tough and durable, require special handling, knowledge, and skill
      Limited “pot life”
      Much more difficult to repair
      Clean-up must be immediate and thorough
    Expensive. Lacquer in spray cans is extremely expensive when the cost is measured in dollars per ounce. Lacquer in bulk is much less expensive, but spray equipment is expensive (gun, compressor, regulators, line dryers, spray booth, mask). State-of-the-art urethane automotive lacquers are very expensive, even in bulk.
  Solvents and diluents: Lacquer thinner for traditional lacquers. Catalyzed lacquers usually require special diluents (follow manufacturers' recommendations). Water for water based lacquers.
  Note: Traditional lacquers are evaporative. Catalyzed lacquers are reactive.

## Slide 14
Varnish
  Examples:
    Natural oil-based (tung, linseed, etc.)
    Urethane-based (polyurethane)
    Blends
    “Spar” (flexible)
    Catalyzed
    Etc.
  Advantages:
    Many different chemical compositions to choose from
    Can be exceedingly tough, especially catalyzed urethane varnishes
  Disadvantages:
    Relatively difficult to apply
      Not easily sprayed
      Tricky to brush
      Difficult cleanup
    Not easy to recoat. Must be “roughed” before recoating
    Difficult or impossible to repair (may require sanding to bare wood and starting again from scratch)
    Membrane finish
    Usually toxic until completely dry. Vapors of some diluants are quite toxic.
  Dilutant: Mineral Spirits for traditional varnishes. Catalyzed varnishes often require special diluents. Follow manufacturer’s recommendations.
  Notes: Use only gloss varnish. The flatting agents in satin varnishes usually compromise the finish to some degree. If a satin finish is desired, use gloss varnish, allow the finish to dry hard, then rub the finish with an abrasive to produce the desired glossiness.

## Slide 15
Sources of Supply
Easy Cast Clear Casting Epoxy, Hobby Lobby, others
Trans-Tint Dye, Woodcraft, others
Pipettes, numerous internet sources
30 ml measuring cups, numerous internet sources
Deftoil Danish Oil Finish, clear, McGuckin Hardware, Boulder, other sources
Minwax Wipe-On Poly, Clear, Woodcraft, others
Mirka Abralon 2000 grit foam-backed abrasive, Woodcraft, others
Titanium dioxide, make-up supplies, numerous internet sources
6 mil polypropylene sheeting, numerous internet sources
Heat sealers (to seal polypropylene bags), Amazon, numerous internet sources
Nitrile gloves, Costco, numerous internet sources
General finishing supplies, Woodcraft, Homestead Finishing Products
Book, Finishing by Jeff Jewitt, Taunton Press

## Slide 16
Finishing
Tom Wirsing
September 5, 2013